## Slide 1
Process Equipment Used For Brewing
Prof. John D. Sheppard
Dept. of Food, Bioprocessing and Nutrition Sciences

## Slide 2
Milling Mashing/lautering Boiling Fermenting
Packaging Carbonating Clarifying Maturing
START
Tap room
The Brewing Process
Cold storage

## Slide 3
Milling Mashing/lautering Boiling Fermenting
Packaging Carbonating Clarifying Maturing
START
Brewery Capacity

## Slide 4
1. Grain Storage and Milling
Exterior Silos
25 kg bags
Wet milling
Dry milling
Circulated steeping vat
Mash Tun
Water
Mash Tun
Auger
Roller mill

## Slide 5
Brewery Capacity
Operation | Time required
Mashing (all grain) | 1.0 – 1.5 hrs
Lautering | 1.0 – 1.5 hrs
Boiling | 1.0 – 1.5 hrs
Total brewhouse | 3.0 – 4.5 hrs
Fermentation (Ales) | 5 – 7 days
Maturation (Ales) | 2 – 7 days
Fermentation (Lagers) | 7 – 10 days
Maturation (Lagers) | 7 – 35 days
Carbonation | 2 – 5 days
Total product cycle (ales) | 9 – 17 days
Total product cycle (lagers) | 16 – 50 days

## Slide 6
What’s the Bottleneck?
Brewhouse capacity: 20 bbl*
Fermentation capacity: 3 x 20 bbl
(no maturation)
Bright tank capacity: 20 bbl
* 1 bbl of beer is 31 US gal.

## Slide 7
What’s the Bottleneck?
Brewhouse capacity: 20 bbl*
Fermentation capacity: 3 x 20 bbl
Bright tank capacity: 20 bbl
* 1 bbl of beer is 31 US gal.
Time for 60 bbl
12 hrs
5 days
9 days

## Slide 8
What’s the Bottleneck?
Brewhouse capacity: 20 bbl*
Fermentation-maturation capacity: 3 x 20 bbl
Bright tank capacity: 20 bbl

## Slide 9
What’s the Bottleneck?
Brewhouse capacity: 20 bbl*
Fermentation-maturation capacity: 3 x 20 bbl
Bright tank capacity: 20 bbl
Time for 60 bbl
12 hrs
10 days
9 days

## Slide 10
2. The Brewhouse
A 3-vessel 5 BBL Brewhouse in the Wolfpack Brewery

## Slide 11
2-vessel system
Mash/lauter combo
Kettle/whirlpool combo
Kettle/whirlpool combo
3-vessel system
Mash tun
Lauter tun
Brewhouse Configurations

## Slide 12
Malt hydrator
Mash water
input
Grain bed
Rakes for stirring and spent grain discharge
Nozzles for
sparge water
Wort output
Spent grain removal
Slotted false bottom
Mash/lauter Tun Details

## Slide 13
Other Brewhouse Equipment
Control systems
Pumps
Hot liquor tank
Heat exchanger
Aerator

## Slide 14
Fermentation
Conical fermenter tanks (uni-tanks) can be used for both primary fermentation and beer maturation.
Small-medium size breweries use glycol cooling in jackets, while large breweries use temperature-controlled rooms.

## Slide 15
Clarification
Following fermentation-maturation, removal of yeast and other suspended solid material can be accomplished with the use of sedimentation, filtration or centrifugation.
Plate and frame filter (40 x 40 cm)
Continuous disk-stack centrifuge

## Slide 16
Carbonation
Clarified beer is transferred to the jacketed bright tank where it is stored under pressure (10 – 15 psig of gaseous CO2) at low temperature (2 – 4oC) for several days prior to packaging.

## Slide 17
Packaging
Stainless steel kegs:
5.2 gallon (approx. 1/6 of a BBL – sixtel)
15.5 gallon (1/2 BBL)
7.75 gallon (1/4 BBL – reduced height)